## Slide 1: DCAF Under the Hood
Benjamin Celis

## Slide 2: Abstract
The Distributed Control and Automation Framework (DCAF) is an open-source LabVIEW framework designed to create control systems that are reliable, modular, and configurable. In this presentation we will explore the decisions behind the design as well as their implementation. We will cover in detail the data transfer mechanism, execution paradigms, and module reuse.

## Slide 3: Agenda
Introduction
The Tag Bus
DCAF Modules
DCAF Engine
Cool Details:
  VI Packages
  Syslog
  Text to object DVR
  Graphviz

## Slide 4: Distributed Control and Automation Framework (DCAF) Overview
An open-source LabVIEW framework for creating configurable, latest value, data engines that can acquire data from multiple input sources, process that data, and then route it back to outputs or to data services.
Input
Process
Output
Engine
Outside
Outside
Outside
Notes: The Tag Bus Data Framework or TBDF is an open-source LabVIEW framework for creating configurable, latest value, data engines that can acquire data from multiple input sources, process that data, and then route it back to outputs or to data services. It provides a scalable and extensible plugin architecture. It supports users in the development of new plugins with a variety of templates… …and the framework was designed to allow plugins to be reused easily across projects. Reuse is easy because each plugin can define configuration parameters which can be specified using a configuration editor. This also allows plugin behavior to change across multiple deployments of the same application. While applicable to a wide variety of use-cases, the framework was primarily built for applications using a lot of single point I/O: things like control data or industrial communication protocols. The plugin architecture helps facilitate multideveloper teams, and the framework handles the intricacies of execution timing and error handling for its users. Finally, while the framework can run on RT, Windows, and Interact with FPGAs, it was built primarily for applications executing on a real-time OS.

## Slide 5: The Tag Bus
What's the need?
Limited Solutions:
  Variables
  CVT
Scope
Data Types

## Slide 6: Modules
Module Parts
Abstraction Layers
Module design

## Slide 7: DCAF Execution

## Slide 8: Asynchronous Loops

## Slide 9: VI Packages

## Slide 10: Syslog

## Slide 11: Text to objects DVR

## Slide 12: GraphViz