## Slide 1: Distributed Control and Automation Framework (DCAF)
Static Modules
Benjamin Celis, Simon Perez

## Slide 2: Agenda
What Template to use
Static Module Creation
Script include
Parameters
Initialization

## Slide 3: Static Or Dynamic?

## Slide 4: Static or Dynamic
  Static
  Module developer defines the number of channels available in the module
  Template includes UI ready to use.
  Easier to Create
  Mostly used for processing
Dynamic
Final user can configure the number of channels.
More flexible template
Requires more codding.
More commonly used for input/output

## Slide 5: Defining the Channels
Output
Output
Process
Process
Input
Input
Input
Process
Output
Engine
Outside?
Outside
Outside

## Slide 6: Creating a Static Module
  Create Project through Template
  Creates 3 main classes:
    ModuleName configuration.lvlclass
    ModuleName editor.lvlclass
    ModuleName runtime.lvlclass

## Slide 7: Static Module
Configuration Class:
  Select module options (number of instances, allowable targets)
  Update validate.vi with validation rules
  Update get default error list.vi with default error classifications
Editor Class:
  Select module glyph
Runtime
  Implement User Input.vi, User Process.vi, and/or User Output.vi with custom logic

## Slide 8: Process VI

## Slide 9: User Process

## Slide 10: Get Text

## Slide 11: Project 1
Custom PID
Channels :
  Setpoint
  Out
Choose Icon
Update User Process.
Channel | Data Type | Channel Type
Variable | Double | Process Parameter
Setpoint | Double | Process Parameter
Output | Double | Result

## Slide 12
Exercise 1 Custom PID
Dev Guide 4.1

## Slide 13: Exercise 1: Custom PID
Create module from template
Implement the user process
Test the user process

## Slide 14: Scripting Utility
Need to update the channels?

## Slide 15: Scripting Utility

## Slide 16: Project 1B
Custom PID
Channels :
Update User Process.
Channel | Data Type | Channel Type
Variable | Double | Process Parameter
Setpoint | Double | Process Parameter
Output | Double | Result
P | Double | Process Parameter
I | Double | Process Parameter
D | Double | Process Parameter

## Slide 17
Exercise 2
Channel Scripting

## Slide 18: Exercise 2: Channel Scripting
Update the clusters
Run the script
Channel | Data Type | Channel Type
Variable | Double | Process Parameter
Setpoint | Double | Process Parameter
Output | Double | Result
P | Double | Process Parameter
I | Double | Process Parameter
D | Double | Process Parameter

## Slide 19: Static Module Checklist
    To add a Key Value Pair, modify the get desired keys.vi
    Modify the Apply Key Value Pairs.vi to do something with the data

## Slide 20: User Initialization

## Slide 21: Project 2: State Machine
The starting State is defined in a Parameter
To switch from 1 to 2. Only A is True
To switch form 2 to 3 Only B is True
To switch from 3 to 1 Only C is True
State 1
State 2
State 3

## Slide 22
Exercise 3 State Machine Module

## Slide 23: Exercise 3: State Machine
Create module from template
Add the state to the runtime
Initialize the state
Implement the user process
Test the user process

## Slide 24
Exercise 4 (optional)
Running the state machine in DCAF Engine
Notes: In a DCAF engine use the UI module to interact with the state machine module.

## Slide 25: Exercise 4: Running the state machine in DCAF Engine
Use the UI module to test 2 multiplexers in the runtime

## Slide 26: Conclusions
    Static Modules have their channels and parameters defined by the module developer
    Create the Module from the Static Module
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
    Implement the Input, Processing, and/or Output Methods as needed
    You should do testing and validation of your module (will be discussed in later chapters)