## Slide 1: Distributed Control and Automation Framework (DCAF)
Components
Benjamin Celis, Mathew Pollock, Simon Perez

## Slide 2: Agenda
The Tag Bus
Engine Architecture
Module Architectures
The Configuration Editor Framework

## Slide 3: DCAF Components
Configuration
Runtime
Engine
Configuration Editor
Modules
Templates
Examples

## Slide 4
Tag Bus

## Slide 5: DCAF Package Dependency Diagram
Notes: Useful for navigating Tools Network packages and GitHub Repos
The largest open source LabVIEW development project

## Slide 6: Tag Bus
Current Options
Local Variable
Global Variable
Single
Functional Global Variable
Current Value Table (CVT)
Requirements
Flexibility
Scope
Performance
Notes: DCAF was designed for systems in which the main data transfer is tags.
LabVIEW offers many options to manage tags.
But for design we had 3 main guidelines and they could not be achieved with the current options.
What's the need?
Limited Solutions:
  Variables
  CVT
Scope
Data Types

## Slide 7: Tag Bus
CVT on the wire
Controlled Scope
Data Protection
Fast
Reduced memory copies
Filtering

## Slide 8: Tag Bus - Data Dictionary

## Slide 9: Tag Bus
CVT on the wire
Not a Global
Data Protection
Fast
Reduced memory
Filtering
Tag Manipulation
Tags are Objects

## Slide 10: Tag Bus - Duplication
Notes: Major issue with clustersauruses: data copies of the cluster and accidentally stomping on data, especially if sending the whole cluster into every user of the cluster
Solution: break up the cluster such that each user of the cluster gets the minimum data set it needs and prevent useless data copies when getting/setting the values from the main cluster
Each DCAF module gets a “mini” tag bus containing only the data used by that module. Scripting templates take care of all data access operations on the mini-tag bus in the module for most common use cases.
Use of in-place operations, plus never branching the main tag bus wire, prevent copies of the main cluster

## Slide 11
Engine

## Slide 12: DCAF Engine
Output
Output
Process
Process
Input
Input
Input
Process
Output
Engine
Outside?
Outside
Outside
Init
Close

## Slide 13: DCAF Engine
Blue: Provided out of the box
Yellow: Modules to customize behavior
Green: Parallel to the framework
Engine
Editor
Modules

## Slide 14: Engine Execution Model
DCAF Execution Engine
Inputs
Plugin1
Plugin2
Process
Plugin3
Plugin4
Outputs
Plugin1
Plugin5
Upkeep
Fault Recovery
Run State
House-Keeping
Shutdown
Idle
Configuring
Safe State
Tag Bus
Wait
Notes: State machine with a safe state
Sequentially executes Input, Process, and Output methods of each plugin
Passes latest value data between plugins
Configurable execution timing
Built-in error reporting and recovery
Prevent Race conditions, memory allocations, thread starvation, etc.

## Slide 15: Simplified Engine
Engine
Editor
Modules

## Slide 16: DCAF Execution Engine
Engine
Editor
Modules
Notes: The source code for the engine isn’t as scary as you might think. It follows a pretty straightforward sequence of steps:
Check for a message to stop.
Wait for next clock source to fire.
Sequentially read all inputs and store data on the bus.
Process data and store on bus, then process again and store on the bus, then process again. Etc.
Send data to all output locations sequentially.
Choose which plugins execute on the next iteration.
Check for errors and handle them.
Sequential execution provides predictable behavior.
C:\Program Files (x86)\National Instruments\LabVIEW 2017\vi.lib\NI\DCAF\Engines\Standard Engine\Execution Engine\main engine\primary control loop.vi

## Slide 17: DCAF Execution Engine Interface
Can execute have multiple engines at the same time
Each Engine is a different thread
Engine controls modules execution and data transfer
Provides API to control and get access to the engines
Engine
Editor
Modules

## Slide 18: DCAF Execution Engine Interface
Can execute multiple engines at the same time
Each Engine is a different thread
Engine controls modules execution and data transfer
Provides API to control and get access to the engines

## Slide 19: Simplified Engine
Engine
Editor
Modules

## Slide 20: Asynchronous Module
Engine
Editor
Modules

## Slide 21: Asynchronous Module
Modules
Engine
Wait 0 ms on Input Buffer
Get DVR
Polling
Lock DVR
Transfer Data
Write DVR to
Command FIFO
Polling
Wait -1 on Command FIFO
Get DVR
Blocking
Lock DVR
Run Module Input
Write DVR to
Input Buffer
Blocking
Engine
Async Worker
Engine
Editor
Modules
Notes: There is no data transfer, the only thing we are transferring is the DVR. We are using the FIFOs as a arbitration mechanism to protect the DVR. This is required because DVR, will always block and there are no timeouts.

## Slide 22: Asynchronous Modules
Creates DVRs
Creates RT FIFOs
  Command FIFO
  Input, Output and Process Buffer
Launches Asynchronous Worker
Engine
Editor
Modules
Notes: C:\Program Files (x86)\National Instruments\LabVIEW 2018\vi.lib\NI\DCAF\Engines\Standard Engine\Execution Engine\async executor\start async worker.vi

## Slide 23: Asynchronous Module
Engine
Editor
Modules
Notes: C:\Program Files (x86)\National Instruments\LabVIEW 2018\vi.lib\NI\DCAF\Engines\Standard Engine\Execution Engine\async executor\async input data method.vi
C:\Program Files (x86)\National Instruments\LabVIEW 2018\vi.lib\NI\DCAF\Engines\Standard Engine\Execution Engine\async executor\async worker process.vi

## Slide 24
Modules

## Slide 25: Module Components
Configuration
Editor node
Runtime
Configuration
Created on PC, passed to runtime system
Provides data access and serialization/deserialization methods
Data storage only, no editor or runtime logic
Runtime Node
Initializes runtime based on configuration
Provides execution logic
Engine
Editor
Modules

## Slide 26: Module Components
Editor Node
User interface
Runs on PC
Creates or modifies the configuration
Contains the configuration class
Engine
Editor
Modules
Configuration
Editor node
Runtime

## Slide 27: Module Runtime
Engine
Editor
Modules

## Slide 28: Module Runtime Test Harness Example
Engine
Editor
Modules
Notes: Add compare between expected and read values to demo test

## Slide 29: What is the module doing?
Input
Process
Output
Engine
Outside
Outside
Outside
Engine
Editor
Modules

## Slide 30: What is the module doing?
Engine
Editor
Modules

## Slide 31: Static Module
Configuration Class:
  Select module options (number of instances, allowable targets)
  Update validate.vi with validation rules
  Update get default error list.vi with default error classifications
Editor Class:
  Select module glyph
Runtime
  Implement User Input.vi, User Process.vi, and/or User Output.vi with custom logic
Engine
Editor
Modules

## Slide 32: Dynamic Module
Configuration Class:
Editor Class:
Runtime
Engine
Editor
Modules

## Slide 33
Configuration Editor

## Slide 34: Configuration Editor Framework (CEF)
Open Source Library
Tools to manage tree control and subpanels
Can be extended and customized
3 starting templates available
Engine
Editor
Modules

## Slide 35: Configuration Editor Framework (CEF)
Engine
Editor
Modules

## Slide 36: Text to objects DVR
This Feature is from CEF (Configuration Editor Framework)
Allows accessing objects from a string store on a tree