## Slide 1: Distributed Control and Automation Framework (DCAF)
Designing an Application with DCAF
Benjamin Celis, Mathew Pollock, Simon Perez

## Slide 2: Agenda
What should be a module?
  How many Modules do I need?
Interacting with code outside the engine

## Slide 3
What should be a Module?

## Slide 4: What Should be a Module
Modules should operate on latest value (Tag) data
They should generate new values, modify existing values, or route values
Communicating stream data between modules may not be a good fit

## Slide 5: What Should be a Module
Application Specific vs Reusable
  Application Logic could be within a module or outside of DCAF
  Consider making a module into a state machine for control
  Remember the state machine should not block
  Do not hold state data in the module unless there can be only one instance

## Slide 6: How many modules?
If two modules must always be used with each other, consider combining them.
Custom Input Module 1
Custom Process Module 1
Scan Engine Module
Engine
Outside
Outside
Custom Input And Process
Scan Engine Module
Engine
Outside
Outside

## Slide 7: How many modules?
If multiple combinations are possible, keep them separate
Custom Input Module 1
Custom Process Module 1
Scan Engine Module
Engine
Outside
Outside
Shared Memory Module
Custom Process Module 1

## Slide 8
CVT

## Slide 9: DCAF Project Templates
Notes: Application templates exist in addition to the plugin templates.

## Slide 10: Running the Configuration

## Slide 11: Coding outside DCAF
Example loop from the project template
Only need to call the engine and check, other code can run alongside as needed

## Slide 12: Coding outside DCAF - CVT
Input
CVT
Output
Engine
Engine API
Other LabVIEW Code
CVT Variables
Main VI

## Slide 13: Coding outside DCAF - CVT
To get Tag Data out of DCAF into the same main application, use CVT
Pass the Tag to the CVT Module

## Slide 14: Coding outside DCAF - CVT
Read the Tag with the CVT API
Use the Tag data in your application

## Slide 15
Shared Memory

## Slide 16: Shared Memory
DCAF can access Linux Shared Memory through a standard Module
Tags can then be accessed from LabVIEW or other languages

## Slide 17: Shared Memory
Notes: Application templates exist in addition to the plugin templates.