## Slide 1: Distributed Control and Automation Framework (DCAF)
Introduction to DCAF
Benjamin Celis, Mathew Pollock, Simon Perez

## Slide 2: Agenda
Introduction
  Why should you use DCAF?
  Who should use DCAF?
The DCAF Paradigm
  Engine
  Modules
  Configuration
Tools and Externalities
Nomenclature

## Slide 3
Introduction

## Slide 4: Programming Embedded Control Applications is Hard
RT, FPGA, and user interface programming
Distributed I/O and execution
High cost of failure
  Execution guarantees
  Understand failure root cause
High availability
System commissioning
Software updates and deployments
Multi-developer teams
Error handling
Plus the crazy things it actually has to do!
Power Conversion Equipment
Manufacturing Machines
Oil and Gas
Aero Space
Notes: RT, FPGA, and UI programming can vary widely in style and knowledge requirements. Being proficient in all three takes both training and experience.
Distributed I/O and execution means a variety of communication protocols to learn. CAN, EtherCAT, UDP, TCP, AMQP, and possibly even the upcoming IIoT protocols may all be involved.
Execution guarantees require knowledge of deterministic programming techniques. Understanding why something failed requires built-in diagnostics and good error handling.
High availability means programs need to be able to run for months or longer without stopping. They also need to be able to recover from a failure automatically.
No two machines are exactly the same. Tuning, features, parameters often need to be tweaked during setup. This requires extensive and powerful parameterization, which ideally is built into the code before it is needed.
These machines are typically built to last. Development teams need a strategy for how to get updates to the code. How do bug fixes or new features get deployed reliably?
These systems are often complex enough and with a tight enough timeline to require multiple software developers. Multi-developer teams don’t work efficiently overnight, and require training and process investments to really flourish.
To top it all off, the functionality for these machines in terms of their primary tasks are complex and getting even more so. It also needs to do those tasks better than the competition.

## Slide 5: Distributed Control and Automation Framework (DCAF) Overview
Scalable and extensible plugin
architecture
Develop with plugin templates
Reuse existing plugins
Define and configure plugin
parameters
An open-source LabVIEW framework for creating configurable, latest value, data engines that can acquire data from multiple input sources, process that data, and then route it back to outputs or to data services.
Create higher quality control applications, in less time.
Single point I/O, processing, and
data services
Rules for correct-by-construction
software
Configure timing and error handling
Optimized for real-time execution
Notes: The Tag Bus Data Framework or TBDF is an open-source LabVIEW framework for creating configurable, latest value, data engines that can acquire data from multiple input sources, process that data, and then route it back to outputs or to data services. It provides a scalable and extensible plugin architecture. It supports users in the development of new plugins with a variety of templates… …and the framework was designed to allow plugins to be reused easily across projects. Reuse is easy because each plugin can define configuration parameters which can be specified using a configuration editor. This also allows plugin behavior to change across multiple deployments of the same application. While applicable to a wide variety of use-cases, the framework was primarily built for applications using a lot of single point I/O: things like control data or industrial communication protocols. The plugin architecture helps facilitate multideveloper teams, and the framework handles the intricacies of execution timing and error handling for its users. Finally, while the framework can run on RT, Windows, and Interact with FPGAs, it was built primarily for applications executing on a real-time OS.

## Slide 6: Who should use the framework?
New developers in LabVIEW:
  Allows them to work on what the application has to do, rather than how they have to do it.
  Abstracts Real Time concepts for the user
  Provides a configurable I/O Abstraction layer
  Forces good programing practices
Advanced developers:
  Efficient data mapping engine
  Extensible configuration interface
  Excellent code reuse between projects
  Know LabVIEW but doesn’t want to write too much architecture
  Open source and distributed in components that are useful individually

## Slide 7: Who is DCAF for?
Control
Solution
LabVIEW
Application Type: Control and Automation
Single-point I/O, processing, and services
Outputs provided in real-time
Not Real-Time Test
Not Monitoring or Data Acquisition
Scope Type: Deployed Solution
Built product (internal or external)
Project time measured in months
Not a Simple Demo/POC
Tool Type: LabVIEW
Some LabVIEW experience needed
Shared memory integration with C/C++ apps
Not Ladder/61131 developers
Notes: DCAF was designed specifically to help people build better control solutions in LabVIEW. There are plenty of other ways to take advantage of the framework and its components in other applications areas, but control is the main target today. The last thing we want is for anyone to use the framework for the wrong job.

## Slide 8
The DCAF Paradigm

## Slide 9: DCAF Components
Configuration
Runtime
Engine
Configuration Editor
Modules
Templates
Examples
Project Templates
Notes: From DevGuide
**Engine**: State machine that executes *Modules* as defined in the *Configuration Editor* and provides a namespace for *Tags*. The Engine also passes data between its *Modules* according to its *Mappings*.
**Module**: A collection of code of varying functionality that executes within an *Engine* and that can interact with the *Tags* of that *Engine*. Some standard *Modules* are installed with DCAF, but users can also create their own.
**Configuration Editor**: A LabVIEW program used to visually define the functionality of each *Engine* and *Module* in DCAF.

## Slide 10: DCAF Components
Engine: State machine that executes Modules as defined in the Configuration Editor and provides a namespace for Tags. The Engine also passes data between its Modules according to its Mappings.
Module: A collection of code of varying functionality that executes within an Engine and that can interact with the Tags of that Engine. Some standard Modules are installed with DCAF, but users can also create their own.
Configuration Editor: A LabVIEW program used to visually define the functionality of each Engine and Module in DCAF.
Engine
Editor
Modules

## Slide 11: Module Components
Configuration
Created on PC, passed to runtime system
Provides data access and serialization/deserialization methods
Data storage only, no editor or runtime logic
Runtime Node
Initializes runtime based on configuration
Provides execution logic
Configuration
Editor node
Runtime
Engine
Editor
Modules

## Slide 12: Module Components
Editor Node
User interface
Runs on PC
Creates or modifies the configuration
Contains the configuration class
Configuration
Editor node
Runtime
Engine
Editor
Modules

## Slide 13: Module Runtime
Engine
Editor
Modules

## Slide 14: DCAF Modules
Existing
Modbus
Scan Engine
UDP
LED
Profibus
Ethernet/IP
Scaling
Tag Select
UI
CVT
TDMS
…
In Work
FPGA
Alarms
OPC UA Client
TSN
New
DDS
J1939
Shared Memory
PID
Engine
Editor
Modules

## Slide 15: DCAF Engine
Output
Output
Process
Process
Input
Input
Input
Process
Output
Engine
Outside?
Outside
Outside
Engine
Editor
Modules
Init
Close

## Slide 16: Engine Execution Model
DCAF Execution Engine
Inputs
Plugin1
Plugin2
Process
Plugin3
Plugin4
Outputs
Plugin1
Plugin5
Upkeep
Fault Recovery
Run State
House-Keeping
Shutdown
Idle
Configuring
Safe State
Tag Bus
Wait
Notes: State machine with a safe state
Sequentially executes Input, Process, and Output methods of each plugin
Passes latest value data between plugins
Configurable execution timing
Built-in error reporting and recovery
Prevent Race conditions, memory allocations, thread starvation, etc.

## Slide 17: Simplified Engine
Engine
Editor
Modules

## Slide 18: Tag Bus
Current Options
Local Variable
Global Variable
Single
Functional Global Variable
Current Value Table (CVT)
Requirements
Flexibility
Scope
Performance
Engine
Editor
Modules
Notes: DCAF was designed for systems in which the main data transfer is tags.
LabVIEW offers many options to manage tags.
But for design we had 3 main guidelines and they could not be achieved with the current options.
What's the need?
Limited Solutions:
  Variables
  CVT
Scope
Data Types

## Slide 19: Tag Bus
CVT on the wire
Controlled Scope
Data Protection
Fast
Reduced memory copies
Filtering

## Slide 20: Tag Bus - Data Dictionary

## Slide 21: Tag Bus - Duplication
Notes: Major issue with clustersauruses: data copies of the cluster and accidentally stomping on data, especially if sending the whole cluster into every user of the cluster
Solution: break up the cluster such that each user of the cluster gets the minimum data set it needs and prevent useless data copies when getting/setting the values from the main cluster
Each DCAF module gets a “mini” tag bus containing only the data used by that module. Scripting templates take care of all data access operations on the mini-tag bus in the module for most common use cases.
Use of in-place operations, plus never branching the main tag bus wire, prevent copies of the main cluster

## Slide 22: Configuration Editor Framework (CEF)
Open Source Library
Tools to manage tree control and subpanels
Can be extended and customized
3 starting templates available
Engine
Editor
Modules

## Slide 23
Getting Started

## Slide 24: Getting Started
Create a project with the Execution Template
Open the Editor from the Tools menu
Configure the system in the Editor
Populate Includes VI
Save the Configuration
Load the Configuration using the template VI.

## Slide 25: DCAF Project Templates
Notes: Application templates exist in addition to the plugin templates.

## Slide 26: Running the Configuration

## Slide 27
Resources

## Slide 28: Resources
ni.com/DCAF
  Getting started material
  Support forum
github.com/LabVIEW-DCAF
  Issue reporting
  Pull requests welcome!

## Slide 29: DCAF Package Dependency Diagram
Notes: Useful for navigating Tools Network packages and GitHub Repos
May be the largest open source LabVIEW development project