## Slide 1: Distributed Control and Automation Framework (DCAF)
Static Modules
Benjamin Celis, Mathew Pollock, Simon Perez

## Slide 2: Agenda
What is a Static Module
When to create a Static module
Common Overrides
Exercise Module
Recruiting Modules ( ? )

## Slide 3: What are Static Modules?

## Slide 4: Static Module
  What information needs to be configurable?
  Application specific modules will have a number of inputs and outputs that do not change.
  Therefore, use the Static Module Template

## Slide 5: Static Module
  Template included with DCAF
    Theoretically there is no underlying difference
  Do not need to create the User Interface for the configuration
  Only need to write the actual logic in specific User Override methods
[image of a project with vi’s highlighted]

## Slide 6: When to create Static Modules?

## Slide 7: Static Module
  Static Number of Inputs and Outputs
  Common for Processing Modules
  Common for fixed application-specific logic

## Slide 8: Creating a Static Module
  Create Project through Template
  Creates 3 main classes:
    ModuleName configuration.lvlclass
    ModuleName editor.lvlclass
    ModuleName runtime.lvlclass

## Slide 9: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Developer’s Guide Checklist

## Slide 10: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Create the Module from the Template

## Slide 11: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Set up the configuration that can be saved and loaded on initiation
Examples
  File Path
  Network address
  Data encoding
Avoid directly modifying the UI

## Slide 12: Static Module Checklist
    To add a Key Value Pair, modify the get desired keys.vi
    Modify the Apply Key Value Pairs.vi to do something with the data

## Slide 13: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Write the Initialization
  Requires modification of the user init.vi and maybe of the init.vi

## Slide 14: Creating a Static Module
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Write the Initialization
  Requires modification of the user init.vi and maybe of the init.vi

## Slide 15: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
If the module requires configuration information, modify the process.vi to pass the runtime.lvclass into the user process.vi

## Slide 16: Static Module Checklist
    Create the Module from the Static Module Sample Project
      Define the Channels
    Add Parameters to set desired keys.vi (optional)
    Handle initialization (optional)
      Handle initialization of references, sessions, parameters
      Pass References into Runtime class if necessary, modify object to allow this
    Implement the Input, Processing, and/or Output Methods as needed
      Modify user process.vi to contain references or the Runtime class if needed and process.vi to pass data necessary to `user process.vi`
      Add Processing code to `user process.vi`
      Add code to input.vi to pass necessary sessions or config data to user input.vi
      Add input code to `user input.vi`.
      Repeat for output
    Programming Considerations for Run-State Methods
      Determinism
      Non-blocking execution
    Specifying other properties
    Testing and validation
Write the Process, Input or Output functionality in the user process.vi, user input.vi or user output.vi

## Slide 17: Static Module
Configuration Class:
  Select module options (number of instances, allowable targets)
  Update validate.vi with validation rules
  Update get default error list.vi with default error classifications
Editor Class:
  Select module glyph
Runtime
  Implement User Input.vi, User Process.vi, and/or User Output.vi with custom logic

## Slide 18: Dynamic Module
Configuration Class:
Editor Class:
Runtime

## Slide 19: Excercise